## Slide 1: Muography with nuclear emulsions – Stromboli and other projects
Valeri Tioukov1, Giovanni De Lellis1, Paolo Strolin1, Lucia Consiglio1, Andrey Sheshukov1, Massimo Orazi2, Rosario Peluso2, Cristiano Bozza3, Chiara De Sio3, Simona Maria Stellacci3, ChiaraSirignano4, Nicola D’Ambrosio5, Seigo Miyamoto6, Ryuichi Nishiyama6, Hiroyuki Tanaka6
1University of Napoli / INFN, Italy, 2INGV - Napoli, Italy, 3University of Salerno / INFN, Italy, 4Universityof Padova / INFN, Italy, 5INFN - LNGS, Italy, 6University of Tokio, Japan

## Slide 2: Emulsion laboratories in Italy
Main business is fundamental Particle Physics (neutrino experiments in particular)
1990 – 2002 CHORUS experiment
2002 – now OPERA project
Emulsion scanning laboratories in Italy (OPERA participants)
  Napoli, Salerno, Gran Sasso, Bari, Bologna, Padova
  About 30 scanning systems were constructed in Italy for OPERA scnning
Since 2011 – some laboratories are involved in Muography projects
  Napoli, Salerno, Gran Sasso

## Slide 3: The OPERA detector: 8.9 mln films with the total emulsion sensitive surface of 200000 m2
neutrino
10x10x50 meters
apparatus
ECC “brick”
57 emulsion plates
56 lead plates
10x12x7 cm, 8 kg

## Slide 4
Unzen
Stromboli
Teide summit
Muography emulsion projects with
contribution of Italian laboratories
Unzen – contributed to data scanning and analysis (2011)
Stromboli – Design, installation and data analysis (2012)
Teide – exposure is completed, scanning is started (2013)
La Palma – modules design, installation, analysis started (2014)

## Slide 5: The principle of muon radiography
Telescope
11/18/2014
Valeri Tioukov, IAVCEI 2013
5
Nearly horizontal
atmospheric muons cross the mountain
It’s assumed that the muon flux and spectrum well known and nearly constant
Assumed the precise knowledge about the mountain shape
What we can obtain is the angular map of the average rock density using the muons absorption information
Detector should provide precise angle for each particle passed through
The method is limited to the upper part of the mountain above the detector
Low muons rate do not allow to have short exposure – months is a typical time scale
1 km of the rock thickness is an approximate upper limit for 1-few m2 detectors with few months exposure
Emulsion is a good candidate!

## Slide 6: Motivations for the Stromboli exposure
Stromboli is one of the most known and most active volcanoes in the world
Great amount of monitoring equipment is installed on the volcano slopes, but the exact internal structure of the region below craters is not well understood yet
There is a possibility that the explosion source mechanism is representative of two cracks dipping ∼60◦ that are located approximately 220-260 m, beneath the active craters, probably representing parts of an echelon system of fissures
muon radiography can be an independent technique for investigating the internal structure of the cone and revealing the location and extent of the conduits that feed the continuous explosions
Region under “Sciara del Fuoco” is the one of our interest
Motivations for muon radiography of active volcanoes,
G. Macedonio and M. Martini, Earth Planets Space, 61, 1–5, 2009

## Slide 8
GPS
Movement sensor
1B
2B
3B
4B
5B
8B
7B
6B
The overall dimension is about 70 x 350 cm, 250 kg

## Slide 9
Emulsions extraction after 5 months exposure. The envelopes are in a good shape

## Slide 10
Metal plates
of 5mm (inox)
Envelopes with emulsions
glued to the central
inox plate
Aluminum Frame
Elastic (rubber) layers
One module with 10 emulsion “cells”
Each cell has 2 emulsions doublets attached
to both sides of the central metal plate.
Front view of the central plate (26 x 80 cm)
The total weight of one module is of 26 kg
Total amount of emulsions/module: 40
The active surface covered is of 1200 cm2
The overall weight of 8 modules and the support frame is about 250 kg
“Exploded view”
Scheme of the internal module structure
Track is defined by 2-4 consecutive segments in 4 plates
x
x
x

## Slide 11: The data analysis assume the precise knowledge about the mountain shape
Detector position
Area of interest
Only the part of the island above
500m is displayed here
Precise and up to date
Digital Elevations Map (DEM) Is important

## Slide 12: Above 500 m part of the island
Detector
Craters region

## Slide 13
1
3
2
To keep memory about the module orientation 3 fixed vertices were installed and the distances measured with the laser distanziometer (+-2 mm accuracy)
GPS data were recorded on 2 detector and on 2 vertex points

## Slide 14
View from the detector position
(640m asl, about 600 m
linear distance to craters)
Craters region (750 m)
Sciara del fuoco

## Slide 15
DEM – Photo comparison
Photographs of the mountain taken from the detector position compared to the shape of the DEM viewed from the same point
Precise images coincidence confirms the precision of the GPS coordinates

## Slide 16
1 SA
2 SA
3 NA
4 TO
5 NA
6 NA
7 NA
8 TO
Data processing
8 modules were scanned and analyzed in 3 laboratories:
Napoli: 3,5,6,7
Salerno: 1 , 2(ny)
Tokyo: 4,8
The data are not perfectly uniform but in the region of interest have similar shape
Analyzed area is of 0.73 m2
Alignment problems
To be solved

## Slide 17
Data
Monte Carlo
All data are superimposed after the module-dependent corrections
On the plots there are tracks slopes.
Positive ty correspond to the Mount direction
Negative ty correspond to the opposite direction – almost free Sky
Normalized to /day/m2
BIN: 0.01x0.01

## Slide 18
Contour line taken at 0.2
For precise definition of the mount shape by muons data the Mount (positive ty) was subtracted from the free Sky (negative ty) and normalized to Sky

## Slide 19
Contour line taken at 0.2
To cross-check the procedure,
the same was done for MC
MC (Sky-Mount)/Sky

## Slide 20
Contour line taken at 1 m
of the muon path in the rock
Rock thickness on the path of muons travelling to the detector
DEM+MC viewer are used. Detector is positioned on the DEM using the coordinates taken from high precision GPS
measurements
From DEM and detector position

## Slide 21
Level of 1 muon/bin defines the theoretical measurement limit
MC flux:
Due to normalization
problem we used data free Sky region close to mountain to normalize MC

## Slide 22
mount edge from DEM&MC
mount edge obtained from data flux
Sensitivity limit (1 muon/bin)
A
B
C
A
B
C
We may define 3 regions in the angular space:
Free Sky
Sensitivity
region
Out of sensitivity
(thick rock, low flux)
mount edge obtained from MC flux

## Slide 23
Data and normalized MC flux are subtracted
We observe significant muons excess in the craters region
A
B
C

## Slide 24: Résumé for the Stromboli analysis
The scanning and data preprocessing are completed
Analysis is in a good shape, the improvements are expected in
  Absolute MC and/or data flux normalization
  Some fine tuning for the efficiency/purity corrections is still possible
Data interpretation from the geological point of view - to be done
General remark: data analysis becomes quite sophisticated due to the fact that we work with 9 years old emulsions which has high background and low efficiency. With new ones data purity and detection efficiency would be be much higher resulting in much higher precision in the flux measurement.

## Slide 25
New compact ECC modules for muography were designed and constructed in INFN Napoli for Canary exposures. These modules were installed in 2014 on La Palma and on Teide mountain.
The modules are precise, robust, reusable and versatile
La Palma, CumbreVieja
Teide

## Slide 26: Potential Italian contribution for future NET Muography projects
Emulsion scanning and analysis. We have huge experience and know how in this field
Mechanical design and installation of emulsion-based detectors – proved by Stromboli and La Palma exposures
Contribution to the data reconstruction analysis and simulation

## Slide 27
La Sciara del Fuoco al tramonto
Thank you for your attention!

## Slide 28: Backup slides

## Slide 29: Example of the elevation profile
1.5 km
640 m
Tan =0.24
Stromboli has not so sharp cone - only a part of edifice can be
monitored with a middle-size muon telescope

## Slide 30
After 5 months of data taking we found the detector in a good shape well protected from sun heating and from moisture by rubber foam (armaflex) and by expanded clay

## Slide 31
DEM – Data comparison
Dem view
Data tx-ty distribution
Dem-data superimposed
Data absorbed part
em-data absorbed superimposed

## Slide 32
The first exercise of data-MC comparison on the incomplete statistics
We observe some data excess in a crater region in respect to MC, this can be a sign of lower density
It is difficult yet to judge about more fine effects
We plan to perform additional study to refine efficiency and background angular dependency corrections
Data subtracted from MC

## Slide 33: Nuclear emulsions as a detector for muon radiography
Advantages
Perfect intrinsic angular resolution (better then 2 mrad)
Compact and easy to transport
No electricity required
Can be installed in a harsh environment
Modular, can be installed inside narrow locations
Disadvantages
No time information (can be solved in some cases)
Complicated and time-consuming data acquisition – required special scanning systems
accepted temperature range for long-term exposures is below 25 C
Single-use sensitive part
Able to provide new information complimentary to
other methods used for volcanoes survey