## Slide 1: The Mu-ray Detector technology

## Slide 2: The “Shadow” of the Vesuvius

## Slide 3: The Basic Module Idea
32 scintillator strips
0.5 m
Opto-electronic connector
to photo-multipliers
WLS optical fibers

## Slide 4: Some Details on Preparation
Arbitrary Unit
Fibers
Scintillators
Optical connector

## Slide 5: Inside The Basic Module
Triangular shape reduce death spaces, gives more strength to the module and allow for charge balance method
Best optical gluing solution were adopted to avoid light losses due to intra-scintillator scattering or wrong coupling with photon detectors

## Slide 6: The Basic Module
The Basic Module is an ensemble of 32 plastic scintillators disposed side by side
Each scintillator has a WLS fiber glued inside
The 32 fibers are collected to the so called optical connector

## Slide 7: Fibers couplings
FIBERS TO SCINTILLATORS
FIBERS TO OPTICAL CONNECTOR

## Slide 8: Bare Telescope
The plane is assembled with 4 modules: 2 used for the X coordinate and 2 for the Y one
A telescope is constituted by 3 planes
With this system we are able to track the trajectory of real muons passing through the telescope and reject the events mimicking muons

## Slide 9: How does it look?

## Slide 10: Trace Muons Through Detection of Light
When a muon passes through the MU-RAY detector, deposits a certain amount of energy, turned into blue light by scintillators. The WLS fibers entrap produced light and lead it to the optical connector where it will be revealed by Silicon PhotoMultipliers (SiPM).
Due to the shape of the scintillators, in each station will be switched on two neighbors X SiPMs and two Y ones and if all the three “points” are aligned the trace correspond to the passage of a real muon
fake m from ‘albedo’
m
fake m from ‘shower’

## Slide 11: Silicon Photomultiplier and SPIROC
SiPM
SLAVE board
Sensors housing board

## Slide 12
Photo-detection efficiency (10%-60%)
Linearity ( if n photons << n cells)
High gain (105-106)
Single photon detection sensitivity
Fast (≈ 1 ns rise time)
Good time resolution (< 100 ps)
Low bias voltages ( < 100 V) very low power consumption (10 mW)
Insensitive to B field
Extremely compact and robust
Breakdown voltage and dark rate depend on temperature
SIGNAL CAPTURED BY FAST SCOPE (AVERAGE MODE) WITHOUT INTERMEDIATE ELECTRONICS
LeCroy SDA 760Zi: 6 GHz
Silicon Photomultiplier in Detail

## Slide 13
Bi-gain low noise preamp
  Low noise charge preamplifier capacitively coupled = voltage preamplifier
  Gain adjustable with 4 bits common to all preamps : Cf=0.1, 0.2, 0.4, 0.8 pF
Positive input pulse
8 mV/pe in High Gain
Noise : 1.4 nV/sqrt(Hz)
Power : 2 mW (unpulsed)
Low gain at preamp level
0.8 mV/pe, MAX : 2000 pe (300pC)
1.5pF
0.1pF-1.5pF
+HV
Si PM
8-bit DAC
ASIC
EASIROC features

## Slide 14
1. 32 CH LOW GAIN, PROGRAMMABLE SHAPING, VOLTAGE MEASUREMENT PATH THAT HAS SAMPLE AND HOLD CAPABILITY
2. 32 CH HIGH GAIN , PROGRAMMABLE SHAPING, LIKE PREVIOUS ONE
3. 32 CH FAST TIMING PATH, WITH COMMON THRESHOLD PROGRAMMABLE COMPARATOR WITH 32 OUTPUTS.
MAIN DATA IN TIMING APPLICATION AND ARE FED TO THE FPGA CHIP TO BE PROCESSED AS REQUESTED.
SiPM BIAS VOLTAGE CAN BE PRECISELY ADJUSTED FOR EACH CHANNEL BY A PROGRAMMABLE 5V DAC
EASIROC main Functions
IN ORDER TO PROPERLY CONFIGURE AND PROGRAMM THE CHIP, 3 REGISTERS CAN BE SERIALLY ACCESSED : «SLOW CONTROL» REG, »READ» REG. , «PROBE» REG.
«OR32» FAST SIGNAL USED TO TRIGGER ACQUISITION SEQUENCE

## Slide 15
SIPM TEST SET-UP using the modified hybrid
USB
MICROCOAX 100 OHM DIFFERENTIAL CONNECTION TO FE-SIPM-PCB
LABVIEW SIMPLE INTERFACE ALLOW TO PROGRAM EASI-ROC CHIP REGISTERS
SLOW CONTROL,
READ AND PROBE REGISTERS
- WE CAN ALSO SET OVER-BIAS FOR EACH SINGLE SIPM THROUGH A DAC SETTING
PC COMMUNICATE THROUGH A USB INTERFACE
EXTERNAL AUXILIARY CIRCUIT TO EASILY TEST AND DEBUG
DISCRETE ANALOG CIRCUIT TO MANUALY ADJUST HOLD TIMING FOR EASIROC CHIP
PRELIMINARY MEASURMENTS MADE WITH A FAST SCOPE
PROGRAMMABLE PREAMPS GAIN
TAB SELECT DIFFERENT REGISTERS
COAX CONNECTOR FOR ANALOG SIGNAL PROBING (BUFFERED)
TRIGGER OUT PROBING AREA
EASIROC BASED DAQ BOARD
FBK-IRST SIPM BONDED ON PCB.
PLACE AVAILABLE ALSO FOR OTHER DETECTORs (HAMAMATSU)
MULTILAYER RIGID-FLEX PCB SUPPORT FOR SIPM DETECTOR WITH GOOD SHIELDING PROPERTIES
EASIROC with single SiPM

## Slide 16
HM TJ2313 Vb=(73.5-1.5)V, I=1.3uA, T=22.4oC Dark
60ns G=14, F2 - maximum.
7 mV / photon
2 photon peak
1 photon peak
100mV/Div
MAX 220mV
20mV/Div
MAX 20-25 mV
4-6 mV / photon
EASIROC tests
FBK
Hamamatzu

## Slide 17: Slave board’s Features
The analog signals produced by SiPMs are converted in digital data
Dynamic tuning of the working point
Onboard pins to read temperature and humidity sensors
Setup for best performances corresponding to environmental conditions
Housing board’s Features
Hosts 32 SiPM and guarantee for best positioning respect to module’s fibers
It has an isothermal surface to setup the same temperature condition to all 32 photomultipliers
Temperature sensors are placed close to the SiPMs
Humidity sensors to not exceed the dew point

## Slide 18: Temperature control system
Based on Peltier cells
Designed to minimize inetrnal temperature variations due to external changes
Sets temperature condition for all housed SiPMs at the same time
Works with passive cooling

## Slide 19: Data Acquisition…
… and Slow Control
SLAVE Boards
PC

## Slide 20: RPi Micro System
MASTER board
Slow Control
Power generators
Thermometer
Hard Disk
Internet

## Slide 21: Full Automation
Main Program (Python3)
Low Level Functions (C/C++)
Data Base (MySQL)
Sensors
Raw data
Apply new settings
Master Board /
Power Supplies
Environment

## Slide 22: Remarks
The construction of the MU-Ray detector starts in the spring of 2011
Tests and experiments to find best materials, sensors, computing and monitoring solutions lead to the development of an automated muon detector
There have been many improvements during its assembly
Other improvements and new features are scheduled for the 2013/14
Its precise calibration and characterization allowed to set for best performance
In April 2013 we “see” the Vesuvius, our hard playground, for the first time and after few days of data acquisition
Other improvements and new features are scheduled for the 2013/14
Since June 2013, the detector is in Clermont Ferrand (France) at the Puy-de-Dome

## Slide 23: The Puy de Dome’s “Shadow”
MuRay - Tomuvol Experiments collaboration in Clermont-Ferrand
(France)

## Slide 24
Thanks
mail :: cimmino@na.infn.it